## Slide 1
Modeling of Active
Aeroservoelastic Systems
Anthony Su
11/30/2023
Notes: Name: Anthony Su
Master’s student here at the Aero+Astro department here at the University of Washington
Advisor: Professor Eli Livne
Thesis: Modeling of Active Aeroservoelastic Systems

## Slide 2
Agenda
Overview
Mathematical Model
FEM & GVT
Wind Tunnel Testing
Conclusion
Model Tuning & Optimization
Notes: Agenda
overview
FEM & GVT
math model
wind tunnel testing
model tuning and optimization
conclusion and questions
Please hold your questions until the end of the presentation (if I go on a tangent I may never return!)

## Slide 3
AEROSERVO-
ELASTICITY
Structural Dynamics
Aerodynamics
Controls
MODELING
Physics-based model
Required for active control
MARGE
Model for Aeroelastic Response to Gust Excitation1
Overview
https://www.m4-engineering.com/wp-content/uploads/2020/04/pynastran-2.png
Notes: Overview
Aeroservoelasticity
structural dynamics, aerodynamics, and controls
important because energy-efficient aircraft have long, slender wings which are very flexible
  the most flexible wings must actively counteract bending and twisting in real-time
    MLA, GLA, and flutter suppression
MARGE
MARGE is the test article that is modeled and tested in this project
short for Model for Aeroelastic Response to Gust Excitation
Modeling
The objective of this project was to synthesize a physics-based state-space model of MARGE
  Physics-based “grey-box” models are (in theory) more interpretable and generalizable than traditional black-box system identification methods
This model can then potentially be used for control design to do the aforementioned things (MLA, GLA, flutter suppression)

## Slide 4
Overview
MARGE
Model for Aeroelastic Response to Gust Excitation1
Low-cost
Highly flexible
Rotates freely in pitch
Notes: MARGE
MARGE: “model for aeroelastic response to gust excitation”
  Designed and built several years ago, see [Quenzer et. al. 2019]
it’s low-cost for an active wind tunnel model
  simple flat aluminum spars
  3D-printed plastic airfoil profile shells
  hobby-grade servos
highly flexible
  first natural frequency 1.4 Hz
rotates freely in pitch
fuselage (a beam)
wing (3D printed shells around a beam)
  tail similar
brass weight on wing tip which increases inertia and reduces the natural frequencies of the wing
everything is suspended from a rigid structure, the “hanging sub-assembly”

## Slide 5
Overview
MARGE
Model for Aeroelastic Response to Gust Excitation1
Low-cost
Highly flexible
Rotates freely in pitch
5 on-board sensors
3 on-board actuators
Notes: 5 on-board sensors
3 accelerometers
1 strain gauge in the wing root
1 hall effect sensor paired with a magnet to measure pitch angle
3 on-board actuators
2 ailerons
1 elevator

## Slide 6
Overview
MARGE
Model for Aeroelastic Response to Gust Excitation1
Low-cost
Highly flexible
Rotates freely in pitch
5 on-board sensors
3 on-board actuators
3x3 Wind Tunnel
Twin controllable upstream gust vanes
Notes: 3x3 wind tunnel
MARGE is designed for testing in the UW 3x3 wind tunnel
  it is mounted suspended from the ceiling of the test section of the wind tunnel
Wind blows from top left to bottom right in this image
Upstream of where MARGE is mounted are two gust vanes
  which can create unsteady flow fields around MARGE

## Slide 7
Why?
Need structural dynamic modal information
Existing FEM was outdated
FEM & GVT
Notes: TIME TARGET: 5 minutes
Why?
Need structural dynamic modal information
  as the base for the structural dynamic model of MARGE
Existing FEM was outdated
  it was made several years ago and was missing some upgraded components

## Slide 8
FEM & GVT
NASTRAN FEM
Spars: Linear beam elements
Fuselage: Linear beam elements
Shells: Rigid elements
Notes: Nastran FEM
disclaimer: I didn’t make the NASTRAN model.
spars are linear beam elements
  (Euler-Bernoulli)
Fuselage is linear beam elements
Aerodynamic shells are represented by rigid elements
Concentrated masses to represent shells and other components (like actuators)

## Slide 9
FEM & GVT
NASTRAN FEM
Spars: Linear beam elements
Fuselage: Linear beam elements
Shells: Rigid
Vanes: Rigid
Tunnel: Rigid
Doublet-lattice theory aerodynamics
  Spline interpolation
Notes: NASTRAN FEM
the finite-element model also included the wind tunnel test sections’ walls and the gust vanes upstream
these were all modeled with rigid elements
doublet-lattice theory is the aerodynamics model used in NASTRAN to compute the aerodynamic loads on MARGE
  doublet-lattice aerodynamics is a generalization of vortex-lattice aerodynamics to unsteady flows
  thus, it is a potential flow model which does not capture viscous or compressibility effects (no drag!)
    no drag is ok because in aeroelasticity we mostly worry about large forces, which are mostly lift
spline interpolation
  these loads are computed on the aerodynamic panels (planar surfaces shown)
  to determine how they affect the structure, the loads have to be transferred to the structural model
    this is done with a spline interpolation of the loads on the aerodynamic panels

## Slide 10
FEM & GVT
GVT
Goal:
  Natural frequencies
  Damping ratios
Notes: GVT
goal:
natural frequencies and damping ratios of the natural modes of the structure
  this is the information that is used to adjust the finite-element model
  see here on the left: an example mode shape
    all motions of MARGE can be expressed as a combination of these independent mode shapes

## Slide 11
FEM & GVT
GVT
Goal:
  Natural frequencies
  Damping ratios
Sensor/actuator placement avoids nodal points of mode shapes
Notes: sensor and actuator placement avoids nodal points of the mode shapes
bottom right: the mode shape image from the last slide
notice: the “2020” location is directly over the antinodal point of this mode shape
notice: several tested points lie close to a nodal point of this mode shape, so they won’t sense very much motion from it
  however, they are well-placed for other mode shapes
  enough points were chosen to capture all modes of interest

## Slide 12
FEM & GVT
GVT
Goal:
  Natural frequencies
  Damping ratios
Sensor/actuator placement avoids nodal points of mode shapes
Postprocessing
  Truncation
  Concatenation
  Subtracting steady-state
Notes: sensor data postprocessing
truncation
  get rid of data we don’t need
    before impact
    after oscillations subside
  <point out on chart>
concatenation
  combine the 3 runs for a test point into one time history
    the chart just shows one run; imagine three of these side by side and you just join them head to tail
    although this doesn’t make sense in the time domain, it doesn’t matter as the next step is to transform to the frequency domain where this doesn’t matter
subtract steady-state
  this comes from sensor calibration error or drift; it needs to be removed before transforming signals to the frequency domain
  <point out on chart>

## Slide 13
FEM & GVT
GVT
Transform to frequency domain
  Chirp Z-transform
Correlation functions
Frequency response function (FRF)
Coherence
Notes: transform to frequency domain
chirp Z-transform
  this is an extension of the fast fourier transform which has some benefits which I will not discuss here
compute correlation functions
  Gxx Gyy = autocorrelation functions for the signals
  Gxy Gyx = cross-correlation functions for the signals
compute frequency response functions (FRF)
  three different ways to do this
    H1 FRF
    H2 FRF
    Hv FRF
    these have their pros and cons, but in this study I use the Hv FRF.
coherence

## Slide 14
example FRF
FEM & GVT
GVT
Transform to frequency domain
  Chirp Z-transform
Correlation functions
Frequency response function (FRF)
Coherence
Peaks  natural frequency
Peak width  damping ratio
  Log-decrement method
Deduce which mode is observed based on which sensors’ FRFs it appears in
Notes: see left: example FRF magnitude (FRF is complex-valued) and coherence
peaks  natural frequency
<point out on chart>
peak width  damping ratio
wider, shorter peak = more damping
narrower, taller peak = less damping
the log-decrement method (also known as the 3 decibel rule) is used to compute damping from the FRFs
deduce which mode is observed based on which sensors’ FRFs it appears in
go back 3 slides to show example

## Slide 15
FEM & GVT
GVT
Adjusted bending and torsional stiffness of FEM elements
Torsional mode is captured
Old | Updated | Experiment | Description
0 | 0 |  | pitching
1.454401 | 1.44397 | 1.422 | wing bending 1
10.51099 | 10.48667 | 10.142 | wing bending 2
 | 19.1997 | 18.094 | wing twisting 1
23.13519 | 21.94804 | 19.893 | fuselage in-plane bending 1
17.81394 | 16.63828 | 19.897 | fuselage bending 1
32.33148 | 32.31077 | 32.545 | wing bending 3
 | - | 51.706 | wing twisting 2
66.02579 | 66.01089 | 60.482 | wing bending 4
69.7988 | 69.29826 |  | wing in-plane bending 1
62.68383 | 60.85218 | 74.521 | fuselage bending 2
Notes: adjusted bending and torsional stiffness of FEM elements
note: lower frequency modes are more important as they are the primary motions MARGE will see.
  especially wing bending 1
torsional mode is captured
<point out on table>

## Slide 16
FEM & GVT
GVT
Adjusted bending and torsional stiffness of FEM elements
Torsional mode is captured
FEM matches experiment better
Notes: FEM matches experiment better
y-axis is the discrepancy between the finite-element model and the experimental result
x-axis the modal frequency
for the key low-frequency modes, the new finite-element model (red) became more accurate than the old model (black)

## Slide 17
Mathematical
Model
Notes: TIME TARGET: 15 MINTUES
Mathematical Modeling
Recall, the goal of this thesis is to obtain a state-space model in the form x rate equals [A]x +[B]u and y equals [C]x+[D]u
It’s now time to dive into the theoretical modeling methods to make this happen

## Slide 18
Math Model
Structural Dynamics
Equations of motion
  Modal coordinates
  and from NASTRAN
  from GVT
Aerodynamics
Aerodynamic influence matrix
  Tabulated also from NASTRAN
Notes: Structural Dynamics
start with the structural dynamic equations of motion expressed in the Laplace domain
  it’s a second-order equation
  q is the structural dynamic state in modal coordinates
    (as mentioned earlier, decomposing any motion of the system into a combination of the modes)
  mass and stiffness matrices [M] and [K] are obtained from the NASTRAN finite-element model
  the viscous damping matrix [C] is a diagonal matrix with the damping ratios obtained from GVT
Aerodynamics
ok, we have the structural dyamic equation. what is the forcing F on the right side?
  the aerodynamic forcing!
    this forcing takes the form of a “aerodynamic influence” matrix [A] multiplying the state
      since, of course, the force on the wing depends on the shape of the wing
  remember the doublet-lattice aerodynamic model from NASTRAN?
    we have tabulated aerodynamic forcing [A] from there at various frequencies
      however, this is not a neat matrix that we can turn into the state-space model we want in the end

## Slide 19
Math Model
Structural Dynamics
Equations of motion
  Modal coordinates
  and from NASTRAN
  from GVT
Aerodynamics
Aerodynamic influence matrix
  Tabulated also from NASTRAN
Rational function approximation
  Roger Approximation3
    Lag constants
    Least-squares regression
Notes: Roger approximation
so, turn to a rational function approximation
  The Roger approximation is a way to approximate a table of aerodynamic influence matrices [A]
    it has these 0th, first and second order terms
    and it accounts for temporal lag effects with these lag terms
    the [P] matrices are what are set to make this fit the [A] matrices
      this is done with a least-squares regression

## Slide 20
Math Model
Plant Dynamics
State vector
  position
  velocity
  lag terms
Reduce order of equations of motion to first-order  state-space model
Notes: plant dynamics
state vector
modal position
modal velocity
lag terms to track those lag effects
  won’t go through how those are defined here
by tracking the model velocities and the lag terms, we can reduce order of the equations of motion to first order
  and after tons of rearranging terms the first order equation comes out to the desired form, x rate = [A]x+[B]u

## Slide 21
Math Model
Plant Output
corresponds to mode shapes from NASTRAN
  accelerometer: motion at one DOF in the mode shapes
  pitch sensor: motion at one DOF in the mode shapes
Notes: plant output
what about the second half of the state-space model y=[B]x+[C]u?
  let’s talk about it
each mode has a mode shape (lets call PHI) which we can get from NASTRAN
  given the modal state vector q, we can obtain the physical shape of MARGE at any point (in the NASTRAN model)
    the pitch for the pitch sensor can be taken as one of these
    the accelerometer requires the acceleration, not the position
      but we have an equation for the modal acceleration that we derived on the previous slide!
        (since velocity is in the state vector and we have the equation for the state rate)
      and the acceleration for the accelerometers can be modeled in this way

## Slide 22
Math Model
Plant Output
corresponds to mode shapes from NASTRAN
  accelerometer: motion at one DOF in the mode shapes
  pitch sensor: motion at one DOF in the mode shapes
corresponds to modal load conditions (force and moment)
  strain gauge: stress at one DOF in the modal loads
  Euler-Bernoulli beam theory
  wing spar thickness
Notes: the modal state q also corresponds to the forces and moments for each mode
  the force at the wing root can be determined
    the strain can be computed using this relation from Euler-Bernoulli beam theory,
      where t is the beam (wing spar) thickness
  strain for the strain gauge output can be thus be modeled in this way
    also as a linear function of the state vector {x}

## Slide 23
Math Model
Plant Output
corresponds to mode shapes from NASTRAN
  accelerometer: motion at one DOF in the mode shapes
  pitch sensor: motion at one DOF in the mode shapes
corresponds to modal load conditions (force and moment)
  strain gauge: stress at one DOF in the modal loads
  Euler-Bernoulli beam theory
  wing spar thickness
Notes: and if we combine all of these (x3 for the acclelerometers) into big matrices which I call [C] and [D], we get the y=[C]x+[D]u we wanted
but why am I calling the state vector and the input vector xp and up so far? …
<next slide>

## Slide 24
Math Model
Actuators & Sensors
Known transfer functions1
  Convert to state-space representation
Approximate perfect sensors:
Coupled Aeroservoelastics
Chain together state-space models
Notes: actuators and sensors
have their own dynamics! (p stands for plant)
  these have to be accounted for in our model or the lag in the actuators and sensors will become (unintended) lag in the model
the actuators have known transfer functions from testing in years past
  can convert them to state-space representation as shown
  and then the output y of the sensors becomes the input u of the plant
  the output y of the plant becomes the input u of the sensors
    but for MARGE the sensors are very responsive so they can be approximated as perfect
coupled Aeroservoelastics
chain together state-space models
  get one large coupled state-space model which looks like <next slide>

## Slide 25
Math Model
Actuators & Sensors
Have their own dynamics!
Known transfer functions1
  Convert to state-space representation
Approximate perfect sensors:
Coupled Aeroservoelastics
Chain together state-space models
Notes: (of course, not showing all the entries in each of these submatrices)
this is our fully derived state-space model!

## Slide 26
Why?
Validate mathematical model
Update mathematical model
Wind Tunnel Testing
Notes: TIME TARGET: 25 MINTUES
Wind Tunnel Testing
Why?
Validate mathematical model (find how well it works)
Update mathematical model (make it work better)

## Slide 27
Wind Tunnel
Test Interface
Simulink Real-Time
National Instruments DAQ
Test Conditions
Pa
mph
Test Plan
On-board control: frequency sweep
Gust vanes: doublet
Three runs for each input for each speed
Notes: Here is MARGE mounted in the 3x3 wind tunnel just outside
suspended from ceiling
test interface
the actuators were controlled using Simulink
the sensor data was read using a National Instruments data acquisition system
  and pulled into Simulink in real-time
test conditions
MARGE was tested at these six airspeeds
test plan
for the ailerons and elevators, frequency sweeps were performed at each speed
for the gust vanes, the doublet response was recorded at each speed
there were three runs for each of these (like in the GVT)

## Slide 28
Wind Tunnel
Postprocessing
Truncation
Concatenation
Subtracting steady-state
Filtering
  Bandpass filter
Transform to frequency domain
Correlation functions
Frequency response function (FRF)
Notes: postprocessing
pretty much the same as the GVT
truncation
concatenation
subtract steady-state component
filtering of accelerometer data with a bandpass filter (not same as GVT)
  this was necessary to eliminate sensor drift and electrical interference in the accelerometers
transform to frequency domain
compute correlation functions
compute FRFs
see left: example experimental time-series data

## Slide 29
Wind Tunnel
Notes: Here is the frequency response for each sensor from each actuator’s input
black = experiment
red = the state-space model
the fit is bad. but this is not the end…

## Slide 30
Why?
Simple model does not yet match messy reality
Model Tuning
Notes: TIME TARGET: 30 MINTUES
Model tuning
Why?
Simple model does not yet match messy reality
The model should be adjusted to better reflect reality (which is the whole point of the model)

## Slide 31
Model Tuning
Tuning Parameters
First wing bending mode natural frequency
  Hz
Damping ratios
Control effectiveness scaling
Roger approximation element-wise scaling
  Roger scaling
Notes: Tuning parameters
were added into the model to be adjusted to do just that
first wing bending natural frequency
damping ratios of all modes
effectiveness scaling of all controls
element-wise scaling of the Roger matrices that were fitted
these all have a range in which they make physical sense
  in structural dynamics, it doesn’t make sense to have a negative damping ratio
  it doesn’t make sense for a control to have negative effectiveness
  etc.
  these will be the constraints that we work in when tunning the model
note: the accelerometer data was deemed too unreliable of a ground truth to fit the model to, so its FRFs are not considered in the tuning process

## Slide 32
Model Tuning
Hand Tuning
Increase pitch damping significantly
Decrease control surface effectiveness
Adjust Roger matrices
Notes: hand tuning
the rigid body pitching mode damping was tuned up a ton
control surface effectiveness was decreased
  (as expected to account for viscous aerodynamic effects)
and some entries of the Roger [P] matrices were adjusted
this fit is much better, but still not great

## Slide 33
Model Tuning
Optimization
Gradient-based optimization
  MATLAB Optimization Toolbox fmincon
Objective function: minimize error
  across all speeds
  across all FRFs
  across all frequencies
  for both magnitude and phase
    favor magnitude correction
https://commons.wikimedia.org/wiki/File:Gradient_descent_method.png
Notes: Optimization
so we turn to optimization to tune the model!
gradient-based optimization using MATLAB
objective function: minimize error
  across all speeds
  across all FRFs
  across all frequencies in those FRFs
  for both magnitude and phase of the complex-valued FRFs (epsilon_mag and epsilon_phase)
    (phase wasn’t shown in those previous plots we just looked at)
  the objective function is a weighted sum of the magnitude and phase error sums
    I optimized this with different values of this weight

## Slide 34
Model Tuning
Notes: Here are the FRFs for some optimized models, along with the manually-tuned model, not-tuned model, and the experimental data.
(default is ns = 2, nLag = 0)
The optimized models fit quite well!

## Slide 35
Higher Fidelity Measurement
Electronically shielded instrumentation
Mode shape measurement
Design and Test Control Law
Gust load alleviation
Maneuver load alleviation
Active flutter suppression
Extend Modeling Techniques
Global optimization
Black-box system ID
Future Work
https://www.m4-engineering.com/wp-content/uploads/2020/04/pynastran-2.png
Notes: Higher Fidelity Measurement
Electronically shielded instrumentation
  MARGE had a lot of sensor signal issues, and electrical interference was suspected to be the culprit for some of it.
  Electronically shielded instrumentation could increase the quality of experimental data and thus the model based on it.
mode shape measurement
  similarly, inaccurate mode shape information was suspected to be a major contributor to the poor initial performance of the model.
Extended Modeling Techniques
global optimization
  two optimization studies I ran, identical except for the initial conditions, reached different solutions
    this indicates that the optimization problem may have local minima that the optimization algorithm can get stuck in
    this could be alleviated by using global optimization methods such as genetic programming to find the global minimum
black-box system ID
  while black-box system identification can be more straightforward to execute in concept, in reality they have some downsides
    one is that they often require a reasonably accurate “starting point” in order to converge to the correct solution
      the results of my work can generate good “starting points” for this purpose
design and test control law
my state-space model can be used for control law design
gust load alleviation
maneuver load alleviation
active flutter suppression
  these active control laws all have the capability of reducing the structural weight required in an aircraft’s structure, and thus increasing performance
  if you are interested in this stuff, go see John’s general exam tomorrow afternoon

## Slide 36
Conclusion
Mathematical model synthesis
Experimental model validation
Applications in aircraft flight control
Notes: In summary:
We derived a methamtical model for MARGE
It was adjusted and using experimental data from GVT and wind tunnel testing
The model produced here has applications in Aeroservoelastic flight controls which can increase the performance of aircraft
Before I open to questions, I would like to ACKNOWLEDGE:
my labmates John and Eddie for answering all my questions,
affiliate professor Marat Mor for lending his expertise in finite-element analysis
  this thesis wouldn’t have been possible without them
and last but not least professor Livne, who taught me everything I know about aeroelastics
Now I will open it up to the audience for any questions:

## Slide 37
References
[1] Jake D. Quenzer, Alison Zongolowicz, Kimberly A. Hinson, Bijan Barzgaran, Eli Livne, Mehran Mesbahi, and Kristi Morgansen. Model for Aeroelastic Response to Gust Excitation. American Institute of Aeronautics and Astronautics Inc., 2019.
[2] Mark B. Tischler and Robert K. Remple. Aircraft and Rotorcraft System Identification, chapter 7. American Institute of Aeronautics and Astronautics, Inc., 1801 Alexander Bell Drive, Reston, VA 20191-4344, 2 edition, 2006.
[3] Kenneth L. Roger. Airplane math modeling methods for active control design. In Structural Aspects of Active Controls, AGARD-CP-228, Aug 1977.

## Slide 38
Notes: I used very soft tip at first which was bad because I was intending to measure up to 200 Hz
I kept on using very soft tip after because I then started decreasing my max freq of interest to practical levels (in the end, maximum area of interest ~20 Hz)

## Slide 39
Notes: why no mode shape measurement?
this is ultimately a modeling study, not a modal testing study. mode shape measurement would be very involved (without a super expensive dedicated system)
MARGE is a low-cost model. It makes sense to use low-cost construction, modeling, measurement, and test.
  otherwise, MARGE begins to be an asset which has a lot of value invested into it and then it becomes just as cumbersome to carefully safeguard as a more expensive, high-quality model

## Slide 40
ENCODE
SANS

## Slide 41
Headings:
ENCODE SANS NORMAL BLACK, ALL CAPS
Alternate headlines and subheads:
UNI SANS BOOK, ALL CAPS
Bodies: Open sans and Open sans bold
FONT GUIDE

## Slide 42
1
2
ENCODE
SANS
UNI SANS
(SUBHEADING)
Or open sans bold body
Open sans regular body

## Slide 43
UNI SANS SUBHEADING
87%
Briefly elaborate on what you want to discuss.
Briefly elaborate on what you want to discuss.
ENCODE SANS HEADING

## Slide 44
1
2
3
ENCODE SANS HEADING
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body
Open sans body

## Slide 45
ENCODE SANS HEADING
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
UNI SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
UNI SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
UNI SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body

## Slide 46
ENCODE SANS
UNI SANS SUBHEADING
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body

## Slide 47
break

## Slide 48
ENCODE SANS HEADING
UNI SANS SUBHEADING

## Slide 49
ENCODE
SANS
UNI SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
UNI SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
UNI SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
01

## Slide 50
ENCODE SANS HEADING
UNI SANS SUBHEADING
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
02

## Slide 51
UNI SANS
Open sans body Open sans body Open sans body Open sans body Open sans body
UNI SANS
Open sans body Open sans body Open sans body Open sans body Open sans body

## Slide 52
ENCODE SANS HEADING
UNI SANS
Open sans body Open sans body Open sans body Open sans body
UNI SANS
Open sans body Open sans body Open sans body Open sans body
UNI SANS
Open sans body Open sans body Open sans body Open sans body
03

## Slide 53
break

## Slide 54
ENCODE SANS
UNI SANS SUBHEADING
UW AERO AND ASTRO
pg 01 / 22

## Slide 55
UNI SANS
UNI SANS
Open sans
Open sans
Open sans
Open sans
Open sans
03
07
08
09
11
ENCODE SANS
13
14
15
16
17
Open sans
Open sans
Open sans
Open sans
Open sans

## Slide 56
OPEN SANS BOLD
Encode sans heading
UNI SANS SUBHEADING
UNI SANS
UNI SANS

## Slide 57
UNI SANS
UNI SANS
OPEN SANS BOLD
Encode sans heading
UNI SANS SUBHEADING
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body

## Slide 58
OPEN SANS BOLD
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
ENCODE SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
ENCODE SANS
UNI SANS
UNI SANS

## Slide 59
OPEN SANS BOLD
ENCODE SANS HEADING
UNI SANS
UNI SANS
UNI SANS
UNI SANS
UNI SANS

## Slide 60
break

## Slide 61
UNI SANS SUBHEADING
ENCODE SANS HEADING

## Slide 62
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
ENCODE SANS

## Slide 63
ENCODE SANS
UNI SANS SUBHEADING
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body

## Slide 64
ENCODE SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
ENCODE SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
ENCODE SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
ENCODE SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body

## Slide 65
ENCODE SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
ENCODE SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body
ENCODE SANS
Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body Open sans body

## Slide 66
break

## Slide 67
ENCODE SANS
UNI SANS SUBHEADING

## Slide 68
Encode sans heading
Open sans body Open sans body Open sans body Open sans body
UNI SANS
UNI SANS
Open sans body Open sans body Open sans body Open sans body

## Slide 69
Encode sans heading
UNI SANS
Open sans body Open sans body Open sans body Open sans body
UNI SANS
Open sans body Open sans body Open sans body Open sans body
UNI SANS
Open sans body Open sans body Open sans body Open sans body

## Slide 70
Encode sans heading
Uni Sans
Open sans body Open sans body Open sans
Uni Sans
Open sans body Open sans body Open sans
Uni Sans
Open sans body Open sans body Open sans
Uni Sans
Open sans body Open sans body Open sans
01
02
03
04

## Slide 71
Item 1
Item 2
Item 3
Item 4
Item 5
50
40
30
20
10
0
Opens sans body Open sans body Open sans body
Encode sans

## Slide 72
Encode sans
Open sans body Open sans body

## Slide 73
break

## Slide 74
Encode Sans
Heading
UNI SANS SUBHEADING
Open sans
NEXT

## Slide 75
Encode sans heading
UNI SANS SUBHEADING
UNI SANS
01
UNI SANS
02
UNI SANS
03
NEXT
OPEN SANS

## Slide 76
UNI SANS
01
Open sans
Open sans
Open sans

## Slide 77
Encode sans heading
Open sans body
Open sans body
Open sans body

## Slide 78
Open sans body Open sans body Open sans body Open sans body. Open sans body
1
2
3
4
Open sans body Open sans body Open sans body Open sans body. Open sans body
Open sans body Open sans body Open sans body Open sans body. Open sans body
Open sans body Open sans body Open sans body Open sans body. Open sans body
Encode sans
NEXT